## Slide 1: Manual Multiply
a data circuit

## Slide 2: Begin building this circuit
build it in modules with the IP you have been working with use RTL
demonstrate to instructor manually with 4 switches for add/shiftRight/Clock/Init
4 switches for multiplier 4 switches for multiplicand

## Slide 3: Use this RTL port interface for the top level data circuit
shiftRight reset loadIn in
clk
D
shiftRight reset loadIn in
clk
D
clk
D
Q
multiplier
out
out
SW 3:0 secondNumberToMultiply
LED 7:4 mostsBits
LED 3:0 leastsBits
SW 13 clk
SW 14 shiftRight
mostsBits
multiplicand
carryIn
carryOut
sum
multiplicand
SW 7:4 firstNumberToMultiply
SW 12 init
SW 15 add
reset
LED 15 addNot
LED 8 carryOut
clear
D
Q
mostBits[0]
addNot
sum
r4bitRightShift
r4bitRightShift
Add
Manual Multiply Vivado Project
D-FlipFlop

## Slide 4: Biggest Challenge of this Project: clock error
Vivado doesn’t want you creating latches.
Vivado wants you to use RTL … so that it can create them. But this is impossible with a manual clock. So in the error message look for this suggestion:
set_property CLOCK_DEDICATED_ROUTE FALSE [get_nets clk_IBUF]
This challenge was experienced in the manually operated D flip flop project.
name of variable associated with ………. always @(posedge clk)

## Slide 5: Add
Has parameters .. see verilog 2012 standard (go to page 88)

## Slide 6: Your tasks
Replace the r4RightShift.v module with RTL verilog >> command Replace the adder.v module with a line of RTL code Add reset … separate from the reset of the r4RightShift module Switch to 8 bits use the diamond buttons to manually step through it Keep the dual use of the multiplier register .. don’t copy the Mano add (page393)